## Slide 1
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p1/12
The Cost of the Critical Path
Rajaraman–Wong delay-oriented clustering · delay, replication and instances
Learning Clustering · original author muranfei (Issue #8) · mapping to Lab 09 (Multilevel) in the teacher's catalogue pending
Notes: This module changes the goal from the cut to delay: the longest path delay of a combinational circuit. Each crossing between clusters adds a fixed delay D to the path, and one logic node may be copied into several clusters. Note: this submission is Lesson 9, while Lab 09 in the teacher’s catalogue is Multilevel; the correspondence awaits confirmation.

## Slide 2
The goal has changed: from cut to delay
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p2/12
Chain P→X→Y→O: δ = 1, inter-cluster D = 3, capacity 2
{P,X} | {Y,O}: 1 crossing, delay 7
{P} | {X,Y} | {O}: 2 crossings, delay 10
Delay follows how often the critical path crosses a boundary
P
1
+0
X
2
+3
Y
6
+0
O
7
1 crossing: delay 7
P
1
+3
X
5
+0
Y
6
+3
O
10
2 crossings: delay 10
Notes: Start with a chain. Both splits respect the capacity, but the first crosses a boundary once, delay 7; the second crosses twice, delay 10. Delay depends only on how many boundaries the longest path crosses, not on how many wires are cut in total.

## Slide 3
The RW model
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p3/12
A combinational DAG; PIs are inputs, POs outputs
Node delay δ(v); 0 on wires inside a cluster, D between
Cluster capacity M (the sum of node sizes)
Logic nodes may be replicated
Goal: minimise the largest PI→PO delay
Here D is the inter-cluster delay, not Module 06's degree matrix.
a
b
c
d
e
f
h
g
i
j
k
l
Candidate data, reconstructed · tie rule assumed
Notes: The RW model is a directed acyclic graph. Each node has a delay, wires inside a cluster add none, wires between clusters add a fixed D, each cluster has a capacity, and nodes may be replicated. The goal is to minimise the largest delay from input to output.

## Slide 4
Replication: logic nodes and instances
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p4/12
One logic node (logicalId) may have several physical instances (instanceId)
An instance is written "node@root"
Replication lets several clusters get the same signal inside
The cost: every copy takes area
A "node → cluster" map cannot express replication
Cluster 1
Cluster 2
i
j
g
g
g@1
g@2
two instances of one logic node
The cost: one more instance, one more unit of area (schematic)
Notes: Replication puts the same logic node into several clusters; each copy is an instance. It lets several clusters get the same signal from inside, but every copy takes area. As data, logic nodes and instances must be recorded separately.

## Slide 5
Initialisation: the candidate DAG and Δ
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p5/12
The original 12-node example: PIs a, b, c; POs k, l
δ = 1, D = 3, capacity 4
Δ(x, v): the longest node delay from x to v (counting v, not x)
Δ(b, k) = 4 (b→e→g→i→k)
The graph is reconstructed from the original film: candidate data
a
b
c
d
e
f
h
g
i
j
k
l
Candidate data, reconstructed · tie rule assumed
Notes: The original 12-node example is reconstructed from frames of the film. Δ is the longest node delay from x to v, counting v but not x; for example from b to k it is 4. This graph is candidate data; the original edge list awaits the original author’s confirmation.

## Slide 6
Labelling: l(v) = max(l1, l2)
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p6/12
Score(x) = l(x) + Δ(x, v)
Candidate cluster: v + the highest-scoring ancestors, up to capacity
Ties: the later in topological order (this course's assumption)
l1 = largest score of a PI inside; l2 = largest score outside + D
i: l1 = 4, l2 = 7 → l(i) = 7
Ancestor
l(x)
Δ
Score
g
3
1
4
inside
e
2
2
4
inside
c
1
3
4
inside
b
1
3
4
outside
f
2
1
3
outside
d
2
1
3
outside
a
1
2
3
outside
l1 = 4, l2 = 7, l(i) = 7
Notes: Labelling handles each node in topological order. Score each ancestor, and put the highest-scoring ones into the candidate cluster up to capacity. l1 is the largest score of a PI inside, l2 the largest score outside plus D. Node i has l1 4 and l2 7, so its label is 7.

## Slide 7
Every label
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p7/12
PIs: l = 1
d, e, f, h: 2; g: 3
i, j: 7
k, l: 8
RW's labels are times, not groups
a
l=1
b
l=1
c
l=1
d
l=2
e
l=2
f
l=2
h
l=2
g
l=3
i
l=7
j
l=7
k
l=8
l
l=8
Candidate data, reconstructed · tie rule assumed
Notes: Every label: the inputs are 1; d, e, f and h are 2, g is 3; i and j are 7; both outputs are 8. RW’s labels are times, entirely different from the group labels of label propagation.

## Slide 8
Recovery: working back from the outputs
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p8/12
Take the candidate clusters of k and l; outside inputs become new roots
8 clusters in all: k, l, d, e, f, h, b, c
20 instances; g, j, e, a have 2 each, b and c 3 each
Every instance has complete inputs
Output arrival 8 = the labels
root k · 4/4
root l · 4/4
root d · 3/4
root e · 3/4
root f · 2/4
root h · 2/4
root b · 1/4
root c · 1/4
g
6
i
7
j
7
k
8
e
5
g
6
j
7
l
8
a
1
b
1
d
2
b
1
c
1
e
2
a
1
f
2
c
1
h
2
b
1
c
1
8 clusters · 20 instances · output 8
Notes: Recovery works back from the outputs: take the candidate clusters of k and l, and the input nodes outside them become new roots, until no new cluster is needed. That gives 8 clusters and 20 instances, every instance has complete inputs, and both outputs arrive at time 8.

## Slide 9
What replication buys
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p9/12
With replication: delay 8, 20 instances
Without: exhaustive search over every capacity-legal grouping, best 10
8 more instances buy 2 units of delay
The optimality result assumes replication is allowed
Replication (RW)
No replication (exhaustive)
Largest delay
8
10
Instances / area
20
12
One best grouping without copies: adfh | bceg | ijkl
Notes: With replication the largest delay is 8, using 20 instances. Forbid replication and search every capacity-legal grouping exhaustively, and the best is only 10. Replication trades area for speed, and the paper’s optimality result assumes exactly that replication is allowed.

## Slide 10
Pseudocode: labelling and recovery
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p10/12
Labelling: topological order; scores, candidate cluster, l1, l2 (Python: rw_label)
Recovery: back from the POs; outside inputs become new roots (rw_reconstruct)
Instances m@r; +0 inside, +D between
Arrival times: evaluate_instance_delay
1
queue
←
every PO
2
while queue is not empty:
3
r
←
pop; select r's cluster
4
outside input u
→
queue (new root)
5
for each selected root r, member m:
6
make instance m@r
7
input inside: u@r
→
m@r (+0)
8
input outside: u@u
→
m@r (+D)
Notes: The pseudocode has two parts: labelling computes scores, candidate clusters and labels in topological order; recovery works back from the outputs, making instances for each selected cluster and connecting the instance wires, adding 0 inside a cluster and D between clusters.

## Slide 11
Limits and open questions
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p11/12
The optimality comes from the paper (IEEE TCAD 1995; DAC 1993) and holds only within its model
The 12-node example is a candidate reconstruction; the tie rule is an assumption awaiting the author's confirmation
This course's tests check consistency and legal instances; they do not prove optimality
Submitted as Lesson 9, while the teacher's Lab 09 is Multilevel: mapping awaits the teacher
Replication costs area; pins, power and more are outside this model
Notes: Finally, the limits: the optimality comes from the paper and holds only within its model. The 12-node example is a candidate reconstruction, and the tie rule is an assumption. This course’s tests only check consistency and legal instances; they do not prove optimality. This submission does not match Lab 09 in the teacher’s catalogue, and the correspondence awaits confirmation.

## Slide 12
Summary
Module 09 · Rajaraman–Wong Delay-Oriented Clustering
p12/12
The goal becomes delay: each crossing adds D to the path.
Labelling gives times, recovery works back from the outputs; logic nodes apart from instances, and replication costs area.
Back to the comparison on the home page: eight modules, eight different operations.
Notes: In summary: the goal becomes delay, and each crossing adds D to the path. Labelling gives each node its earliest time, and recovery works back from the outputs to clusters and instances; logic nodes and instances are kept apart, and replication costs area. Finally, go back to the home page and compare the eight modules.